## Slide 1
Chapter 2
Memory Hierarchy Design
Part 1: The Basics
Computer Architecture
A Quantitative Approach, Sixth Edition
“Ideally one would desire an indefinitely large memory capacity such that any particular … word would be immediately available. … We are … forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
– A. W. Burks, H. H. Goldstine, and J. von Neumann, Preliminary Discussion of the Logical Design of an Electronic Computing Instrument (1946)

## Slide 2: Acknowledgements
Thanks to many sources for slide material
  © 1990 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Architecture: A Quantitative Approach by J. Hennessy & D. Patterson
  © 1994 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Organization and Design by D. Patterson & J. Hennessy
  © 2002 K. Asinovic & Arvind, MIT
  © 2002 J. Kubiatowicz, University of California at Berkeley
  © 2006, © 2010 No Starch Press for Inside the Machine by J. Stokes
  © 2007 W.-M. Hwu & D. Kirk, University of Illinois & NVIDIA
  © 2007-2010 J. Owens, University of California at Davis
  © 2010 CRC Press for Introduction to Concurrency in Programming Languages by M. Sottile, T. Mattson, and C. Rasmussen
  © 2017, IBM POWER9 Processor Architecture by Sadasivam et al., IBM
  © 2016, © 2019 POWER9 Processor User’s Manual, IBM
  © The OpenPOWER Foundation

## Slide 3: Introduction
What do programmers want?
  Unlimited amounts of memory with low latency
Problem:
Fast memory more expensive per bit than slower memory
Solution: Organize memory system into a hierarchy
  Entire addressable memory available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Outcome: Deliver illusion of a fast & large memory to CPU
  How? Temporal locality and spatial locality ensure that nearly all references can be found in smaller memories

## Slide 4: Memory Hierarchy
CPU
Registers
L1
$
L2
$
L3
$
Memory
Disk Storage
Memory
bus
I/O
bus
CPU
Registers
L1
$
L2
$
Memory
FLASH Memory
Memory
bus
I/O
bus
Register
reference
Key: $ = cache
Level 1 $
reference
Level 2 $
reference
Level 3 $
reference
Memory
reference
Disk memory
reference
Register
reference
Level 1 $
reference
Level 2 $
reference
Memory
reference
FLASH memory
reference
Size:
Speed:
1000 bytes
0.3 ns
64 kB
1 ns
256 kB
3-10 ns
8-16 MB
20-30 ns
8-16 GB
80-100 ns
1-8 TB
5,000,000-10,000,000 ns
Size:
Speed:
500 bytes
0.3 ns
64 kB
2 ns
256 kB
10-20 ns
4-6 GB
80-100 ns
256-512 GB
25,000-50,000 ns

## Slide 5: Cache: Multicore Feature of Interest
Introduced in the 1960s as a way to overcome the “memory wall”
  Consequence: Processor outruns memory, leading to decreased utilization
  Memory speeds did not advance as fast as the speed of functional units.
Notes:     Utilization = (ttotal – tidle) / ttotal
Atharva: Extend this graph from 2010 to 2020.

## Slide 6: Idle Time
What happens when you go out to main memory?
Idle time.
  Decreased utilization = less work per unit time
  Idle time = time doing nothing = $$$ wasted
Overcoming the “Memory Wall”
  Caches were not the sole ﬁx for idle time.
  Early Days: Preemptive multitasking and time sharing were actually the dominant methods.
    ... but every program inevitably must go out to memory ... not always enough jobs to swap in while others wait for memory … also, do you really want to be preempted every time you fetch data?
  So, caches important (for now :-) …
Notes:     Utilization = (ttotal – tidle) / ttotal

## Slide 7: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      How much memory bandwidth needed?
      Hint: 64-bit data references & 128-bit instruction references
    DRAM bandwidth is only 25 GB/s (circa 2011-2012)
  How to bridge the gap?
    Multi-port, pipelined caches
    Two levels of cache per core
    Shared third-level cache on chip
Notes:       QUIZ?
      Assuming a 64-bit architecture:
      Data References: 25.6 billion 64-bit data references/second +
      Instruction References: 12.8 billion 128-bit instruction references/second
      = 409.6 GB/s!
      How to bridge the gap? How to give the illusion of a large, fast memory being presented to the processor?

## Slide 8: Caches: An Overview
Traditional Single-Level Memory
Multiple Memory Levels

## Slide 9: Caches: In Action
Access a location in memory
Copy the location and its neighbors into the faster memories closer to the CPU.

## Slide 10: Caches: In Action
Access a location in memory
Copy the location and its neighbors into the faster memories closer to the CPU.

## Slide 11: Caches: In Action
Access a location in memory
Copy the location and its neighbors into the faster memories closer to the CPU.

## Slide 12: Caches: In Action
Access a location in memory
Copy the location and its neighbors into the faster memories closer to the CPU.

## Slide 13: Caches: In Action
Access a location in memory
Copy the location and its neighbors into the faster memories closer to the CPU.

## Slide 14: Caches: In Action
Access a location in memory
Copy the location and its neighbors into the faster memories closer to the CPU.

## Slide 15: Caches: In Action
Next time you access memory, if you already pulled the address into one of the cache levels in a previous access, the value is provided from the cache.

## Slide 16: Caches: In Action
Next time you access memory, if you already pulled the address into one of the cache levels in a previous access, the value is provided from the cache.

## Slide 17: Caches: In Action
Next time you access memory, if you already pulled the address into one of the cache levels in a previous access, the value is provided from the cache.

## Slide 18: Caches: In Action
Next time you access memory, if you already pulled the address into one of the cache levels in a previous access, the value is provided from the cache.

## Slide 19: Caches: In Action
Next time you access memory, if you already pulled the address into one of the cache levels in a previous access, the value is provided from the cache.

## Slide 20: Why Do Caches Work? Locality
Spatial and Temporal
  Locations near each other in space (address) are highly likely to be accessed near each other in time.
Cost?
  A high cost for one access but amortize this out with faster accesses afterwards.
Burden?
  The machine makes sure that memory is kept consistent. If a part of cache must be reused, the cache system writes the data back to main memory before overwriting it with new data.
  Hardware cache design deals with managing mappings between the different levels and deciding when to write back down the hierarchy.

## Slide 21: Caches: Memory Consistency?
What happens when you modify something in memory?

## Slide 22: Caches: Memory Consistency?
What happens when you modify something in memory?

## Slide 23: Caches: Memory Consistency?
What happens when you modify something in memory?
Writes to memory become cheap. Only go to slow memories when needed. Called write-back memory.

## Slide 24: Caches: Memory Consistency?
Eventually written values must make it back to the main store.
When?
  Typically, when a cache block is replaced due to a cache miss, where new data must take the place of old.
The programmer does NOT see this.
  Hardware takes care of all this … but things can go wrong very quickly when you modify this model.
    Example: Cell Broadband Engine, Tilera, and so on.

## Slide 25: Common Memory Models
Shared Memory Architecture
Distributed Memory Architecture
Notes: Which was Intel? Which is AMD? Others?

## Slide 26: Memory Models: Shared Memory
Before
  Only one processor has access to modify memory.
How do we avoid problems when multiple cache hierarchies see the same memory?

## Slide 27: Caching Issues
Assume two processors load
locations that are neighbors,
so data is replicated in the local processor caches.
Now, let one processor modify a value.
The memory view is now inconsistent. One processor sees one version of memory, the other sees a different version.
How do we resolve this in hardware such that the advantages of caches are still seen by application developers in terms of performance while ensuring a consistent (or coherent) view of memory?

## Slide 28: Caching Issues

## Slide 29: Caching Issues

## Slide 30: Caching Issues

## Slide 31: Caching Issues

## Slide 32: Caching: Memory Consistency?
Easy to see “memory consistency” problem if we restrict each cache hierarchy to being isolated from the others, only sharing main memory.
Key insight
  Make this inconsistency “go away” by making the caches aware of each other.

## Slide 33: What is Memory Coherence?
Definition (Courtesy: “Parallel Computer Architecture” by Culler and Singh)
  Operations issued by any particular process occur in the order in which they were issued to the memory system by that process.
  The value returned by each read operation is the value written by the last write to that location in the serial order.
Assumption: The above requires a hypothetical ordering for all read/write operations by all processes into a total order that is consistent with the results of the overall execution.
Sequential Consistency (SC)
  The memory coherence hardware assists in enforcing SC.

## Slide 34: Implicit Properties of Coherence
The key to solving the cache-coherence problem is the hardware implementation of a cache-coherence protocol.
A cache-coherence protocol takes advantage of two hardware features
  State annotations for each cache block (often just a couple bits per block).
  Exclusive access to the bus by any accessing process.
Notes: What does “exclusive access to the bus” imply?

## Slide 35: Bus Properties
All processors on the bus see the same activity.
Every cache controller sees bus activity in the same order.
Serialization at the bus level results from the phases that compose a bus transaction:
  Bus arbitration: The bus arbiter grants exclusive access to issue commands onto the bus.
  Command/address: The operation to perform (“Read”, “Write”), and the address.
  Data: The data is then transferred.
Notes: At what granularity is the data transferred?

## Slide 36: Granularity
Cache coherence applies at the block level.
Recall that when you access a location in memory, that location and its neighbors are pulled into the cache(s). These are blocks.
Note: To simplify the discussion, we will only consider a single level of cache. The same ideas translate to deeper cache hierarchies.

## Slide 37: Cache Coherency via the Bus
Key Idea: Bus Snooping
  All CPUs on the bus can see activity on the bus regardless of if they initiated it.

## Slide 38: Cache Coherency via the Bus
Key Idea: Bus Snooping
  All CPUs on the bus can see activity on the bus regardless of if they initiated it.

## Slide 39: Cache Coherency via the Bus
Key Idea: Bus Snooping
  All CPUs on the bus can see activity on the bus regardless of if they initiated it.

## Slide 40: Cache Coherency via the Bus
Key Idea: Bus Snooping
  All CPUs on the bus can see activity on the bus regardless of if they initiated it.

## Slide 41: Invalidation vs. Update
A cache controller snoops and sees a write to a location that it has a now-outdated copy of.
  What does it do?
Invalidation
  Mark cache block as invalid, so when CPU accesses it again, a miss will result and the updated data from main memory will be loaded. Requires one bit per block to implement.
Update
  See the write and update the caches with the value observed being written to main memory.
Notes: Invalidation-based protocols vs. update-based protocols

## Slide 42: CACHING: UNDER THE COVERS

## Slide 43: Performance and Power
High-end microprocessors have > 10 MB on-chip cache
  Consumes large amount of area and power budget

## Slide 44: AMD Opteron Rev. H Quad-Core
Where are the caches?

## Slide 45: IBM: Power9
Source: IBM

## Slide 46: Sun Niagara
8 cores, 8 threads per core = 64 threads

## Slide 47: Intel Skylake

## Slide 48: Memory Hierarchy: Algorithm
When a word is not found in the cache, a miss occurs
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Lower level may be another cache or the main memory
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address
    block address MOD number of sets

## Slide 49: When to Write Blocks: Strategies to Write to the Cache
Write-Back
Only update lower levels of hierarchy when an updated block is replaced
  On a write miss, the CPU reads the entire block from memory where the write address is, updates the value in cache, and marks the block as modified (aka dirty).
Write-Through
Immediately update lower levels of hierarchy
  When the processor writes, even to a block in cache, a bus write is generated.
  Both strategies use write buffer to make writes asynchronous
Write-back is more efficient with respect to bandwidth usage on the bus, and hence, ubiquitously adopted.
Notes: Write buffer allows the cache to proceed as soon as the data is placed in the buffer rather than wait the full latency to write the data into memory.

## Slide 50: Where to Write Blocks: Associativity
How is the cache organized?
  n-way set associative, where n = # of blocks per set
    Direct-mapped cache (1-way set associative)  one block per set
    Fully associative cache (n-way set associative)  n blocks in one set
    block address MOD number of sets
Tag | Index | Offset
xx | 000 | 00
xx | 001 | 00
xx | 010 | 00
xx | 011 | 00
xx | 100 | 00
xx | 101 | 00
xx | 110 | 00
xx | 111 | 00
Tag | Index | Offset
xxx | 00 | 00
xxx | 01 | 00
xxx | 10 | 00
xxx | 11 | 00
block
address
block
address
Notes: Fully associative (1 set of 8 blocks) | Direct-mapped (8 sets of 1 block) | Set Associative (4 sets of 2 blocks)
32-block main memory. Assume 4 bytes per block.
Assume each block is 4 bytes (for simplicity)
Tag Blk Offset
xx 000 00 block 00000 (0), block 01000 (8), block 10000 (16), block 11000 (24)
xx 001 00
xx 010 00

## Slide 51: Where to Write Blocks: Associativity

## Slide 52: Where to Write Blocks: Associativity

## Slide 53: How to Evaluate Cache Organization: Miss Rate
Miss Rate
  Fraction of cache access that result in a miss
Causes of Misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache

## Slide 54: Other Metrics?
Note: Speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses
Notes: Miss rate can be a misleading measure. Why?
Hence, misses per instruction (rather than misses per memory reference).
Problem with BOTH above measures: Do NOT factor in the COST of a miss.

## Slide 55: Basic Cache Optimizations
Larger block size
  Reduces compulsory misses
  Increases capacity and conflict misses, increases miss penalty
Larger total cache capacity to reduce miss rate
  Increases hit time, increases power consumption
Higher associativity
  Reduces conflict misses
  Increases hit time, increases power consumption
Higher number of cache levels
  Reduces overall memory access time, increases complexity
Giving priority to read misses over writes
  Reduces miss penalty, increases complexity
Avoiding address translation in cache indexing
  Reduces hit time
Notes: Caching must cope with translation of virtual address to physical address.
Common optimization: Use the page offset, i.e., the part that is identical in both virtual and physical addresses, to index the cache.