## Slide 1
Chapter 4
Data-Level Parallelism (DLP) in Vector, SIMD, and GPU Architectures
Part 1: Introduction & Vector Architectures
Computer Architecture
A Quantitative Approach, Sixth Edition
“Who’s first?”
“America.”
“Who’s second?”
“Sir, there is no second.”
-Dialog between two observers of the sailing race later named “The America’s Cup” and run every few years -- the inspiration for John Cocke’s naming of the IBM research processor as “America.” This processor was the precursor to the RS/6000 series and the first superscalar microprocessor.

## Slide 2: Acknowledgements
Thanks to many sources for slide material
  © 1990 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Architecture: A Quantitative Approach by J. Hennessy & D. Patterson
  © 1994 Morgan Kaufmann Publishers, © 2001-present Elsevier
  Computer Organization and Design by D. Patterson & J. Hennessy
  © 2002 K. Asinovic & Arvind, MIT
  © 2002 J. Kubiatowicz, University of California at Berkeley
  © 2006, © 2010 No Starch Press for Inside the Machine by J. Stokes
  © 2007 W.-M. Hwu & D. Kirk, University of Illinois & NVIDIA
  © 2007-2010 J. Owens, University of California at Davis
  © 2010 CRC Press for Introduction to Concurrency in Programming Languages by M. Sottile, T. Mattson, and C. Rasmussen
  © 2017, IBM POWER9 Processor Architecture by Sadasivam et al., IBM
  © 2016, © 2019 POWER9 Processor User’s Manual, IBM
  © The OpenPOWER Foundation
  © 2022, W. Feng, Virginia Tech

## Slide 3: What We Know
What new techniques have we learned that make …
  … control go fast?
  … datapath go fast?
Processor
Control
Datapath
Notes: Control: Multiple fetch; trace cache; branch prediction; out of order; VLIW; EPIC
Datapath: Multiple issue; out of order; branch prediction; predication; speculation; loop unrolling

## Slide 4: Flynn’s Classification Scheme
SISD – single instruction, single data stream
  uniprocessors
SIMD – single instruction, multiple data streams
  single control unit broadcasting operations to multiple datapaths
MISD – multiple instruction, single data stream
  no such machine
  (though some people put vector machines in this category)
MIMD – multiple instructions, multiple data streams
  a.k.a multiprocessors (SMPs, MPPs, clusters, NOWs)

## Slide 5: Continuum of Granularity
“Coarse”
  Each processor is more powerful
  Usually fewer processors
  Communication is more expensive between processors
  Processors are more loosely coupled
  Tend toward MIMD
“Fine”
  Each processor is less powerful
  Usually more processors
  Communication is cheaper between processors
  Processors are more tightly coupled
  Tend toward SIMD
“If you were plowing a field, which would you rather use? Two strong oxen or 1024 chickens?”
- Seymour Cray
Notes: Granularity: Size of chunks of work given to each processor

## Slide 6: The Road Ahead
What’s Up?
  Chapter 4: Data-level parallelism (DLP). Fine-grained parallelism.
    Vector & stream processors
    SIMD extensions: MMX  SSE
    Graphics processing units (GPUs)
What We Just Completed
  Chapter 5: Thread-level parallelism (TLP). Coarse-grained parallelism.
    Multicore
    Multiprocessors
    Clusters

## Slide 7: Introduction to SIMD
SIMD architectures can exploit significant data-level parallelism for
  Matrix-oriented scientific computing
  Media-oriented image and sound processors
SIMD is more energy efficient than MIMD
  Only needs to fetch one instruction per data operation
  Makes SIMD attractive for personal mobile devices
SIMD allows programmer to continue to think sequentially
Introduction
Notes: Power wall leads architects to value architectures that can deliver high performance without the energy and design complexity costs of highly out-of-order superscalar processors.
Vector instructions are ideal. Why?
Increase performance of simple in-order scalar processors without increasing design complexity (and hence, without greatly increasing energy demands).
Allows for slow but wide execution units to achieve high performance at low power.
Independence of elements within a vector instruction set allows scaling of functional units without performing additional costly dependency checks (a la Tomasulo’s)
Can naturally accommodate varying data sizes: 64 64-bit elts, 128 32-bit elts, 256 16-bit elts.

## Slide 8: SIMD Parallelism
Vector architectures (VMIPS, Motorola AltiVec)
SIMD extensions (MMX  SSE  AVX)
Graphics processing units (GPUs)
For x86 processors
  Expect two additional cores per chip per year
  Expect SIMD width to double every four years
  Expect potential speedup from SIMD to be twice that from MIMD
Introduction

## Slide 9: SIMD Parallelism
Vector architectures (VMIPS, Motorola AltiVec)
SIMD extensions (MMX  SSE  AVX)
Graphics processing units (GPUs)
For x86 processors
  Expect two additional cores per chip per year
  Expect SIMD width to double every four years
  Expect potential speedup from SIMD to be twice that from MIMD
Introduction

## Slide 10: Seymour Cray The Father of Supercomputing
An American electrical engineer and supercomputer architect who designed a series of computers that were the fastest in the world for decades..
“Anyone can build a fast CPU. The trick is to build a fast system.”
When asked what kind of CAD tools he used for the Cray-1, Cray said that he liked “#3 pencils with quadrille pads.”
When he was told that Apple Computer had just bought a Cray to help design the next Apple Macintosh, Cray commented that he had just bought a Macintosh to design the next Cray.
In 70s–80s, Supercomputer ≡ Vector Machine
Introduction
Notes: Cray recommended using the backs of the pages so that the lines were not so dominant.

## Slide 11: Scalar vs. Vector
“The basic unit of SIMD is the vector, which is why SIMD computing is also known as vector processing. A vector is nothing more than a row of individual numbers or scalars.”
SIMD Architectures by Jon “Hannibal” Stokes
http://arstechnica.com/articles/paedia/cpu/simd.ars
Representing Vectors
  Multiple items within same data word
  Multiple data words
Introduction

## Slide 12: Vector Code Example
What are the advantages of vector code?
Notes: TWO big advantages to this code: parallel (lots of ILP) and also compact (little instruction bandwidth)
When we get to the SIMD extensions, think about how this vector code might translate to MMX or SSE code.

## Slide 13: Vector Instruction Set
Compact
  one short instruction encodes N operations
Expressive … tells hardware that these N operations:
  are independent
  use the same functional unit
  access disjoint registers
  access registers in the same pattern as previous instructions
  access a contiguous block of memory (unit-stride load/store), or
  access memory in a known pattern (strided load/store)
Scalable
  can run same object code on more parallel pipelines or lanes
Vector Architectures

## Slide 14: Vector Arithmetic
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent (=> no hazards!)
Vector Architectures
Notes: Remember: Computer architecture is all about tradeoffs.

## Slide 15: Vector Instruction
Vector Architectures
Notes: Multiple lanes

## Slide 16: Vector Memory-Memory vs. Vector Register Machines
Vector memory-memory instructions hold all vector operands in main memory
The first vector machines, CDC Star-100 (‘73) and TI ASC (‘71), were memory-memory machines
Vector Architectures

## Slide 17: Vector Memory-Memory vs. Vector Register Machines
Vector memory-memory architectures (VMMA) require greater main memory bandwidth. Why?
VMMAs make it difficult to overlap execution of multiple vector operations. Why?
VMMAs incur greater startup latency.
  Scalar code was faster on CDC Star-100 for vectors < 100 elements.
  For Cray-1, vector/scalar breakeven point was around 2 elements.
Apart from CDC follow-ons (Cyber-205, ETA-10) all major vector machines since Cray-1 have had vector register architectures.
  We ignore vector memory-memory from now on.
Vector Architectures

## Slide 18: Vector Register Architectures
Basic idea
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth

## Slide 19: Vector Register Architectures
Basic idea
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Vector Architectures
VMIPS
(next slide)

## Slide 20: VMIPS
Example architecture: VMIPS
  Loosely based on Cray-1
  Vector registers
    Each register holds a 64-element, 64 bits/element vector
    Register file has 16 read ports and 8 write ports
  Vector functional units
    Fully pipelined
    Data and control hazards are detected
  Vector load-store unit
    Fully pipelined
    One word per clock cycle after initial latency
  Scalar registers
    32 general-purpose registers
    32 floating-point registers
Vector Architectures

## Slide 21: VMIPS Instructions
ADDVV.D: add two vectors
ADDVS.D: add vector to a scalar
LV/SV: vector load and vector store from address
Example: DAXPY
  L.D F0,a ; load scalar a
  LV V1,Rx ; load vector X
  MULVS.D V2,V1,F0 ; vector-scalar multiply
  LV V3,Ry ; load vector Y
  ADDVV V4,V2,V3 ; add
  SV Ry,V4 ; store the result
Requires 6 instructions vs. almost 600 for MIPS
Vector Architectures

## Slide 22: Vector Execution Time
Execution time depends on three factors:
  Length of operand vectors
  Structural hazards
  Data dependencies
VMIPS functional units consume one element per clock cycle
  Execution time is approximately the vector length
Convoy
  Set of vector instructions that could potentially execute together
Vector Architectures
Notes: You can estimate performance of a section of code by counting the number of convoys.
Instructions in a convoy must NOT contain any structural hazards.